## Slide 1
NVIDIA GTC BERLIN · GOLDEN TICKET SUBMISSION
Robot Semantic Memory
Matryoshka embeddings as a gate on expensive perception
A robot shouldn't wake a large vision-language model to answer questions it already knows the answer to. This is a cheap, truncatable visual memory plus a gate that decides when the expensive model isn't needed.
jina-clip-v2 · local, CPU
NVIDIA NIM · VLM + embeddings
NVIDIA Riva · ASR + TTS
github.com/ankursharma435/robot-semantic-memory
Notes: Opening slide. The one-line why is on this slide deliberately — judges asked for the problem stated in one line.

## Slide 2
THE PROBLEM
A robot sees the same
things, over and over.
A warehouse robot stares at the same aisles all day — same shelves, same boxes. But if every question goes to a large vision-language model, it pays full price every time, for answers it already had.
Slow. Power-hungry on a battery. And it occupies the one accelerator the robot has.
COST OF ANSWERING ONE QUESTION
one 11B VLM call
37.4 TFLOP
encode a query locally
9 GFLOP
look it up in memory
128 kFLOP
Estimated as 2 × params × tokens.
Notes: The three-row card sets up the whole argument: the gap between looking something up and asking a big model is five orders of magnitude.

## Slide 3
THE IDEA
One encode. Three memory tiers.
Matryoshka Representation Learning trains the encoder so that any prefix of its output is itself a valid embedding. One forward pass produces 1024 dimensions; the first 64, 256 or 768 each still mean something alone.
short
64d
256 B per frame
what I just saw
decays after 30s
medium
256d
1 KB per frame
what I've learned
labelled, consolidated
long
768d
3 KB per frame
what I know well
durable
Truncation does not make the encoder cheaper. The backbone runs once regardless of how many dimensions you keep. What truncation buys is cheaper storage and cheaper comparison.
Notes: The caveat is on the slide on purpose. It is the first thing a knowledgeable reader tests, and volunteering it buys credibility.

## Slide 4
THE GATE
Knowing when not to ask.
CHEAP
Answer from stored memory
match clears that tier's threshold
returns a label and coordinates
0.058 ms measured
expensive model never invoked
ESCALATE
Wake the expensive model
nothing learned is close enough
or the task needs manipulation
or the match came only from what's in view
sends the live frame to an NVIDIA NIM VLM
Cosine scores from different truncation widths are not comparable — a narrow prefix systematically scores higher. So each tier carries its own threshold, calibrated from photographs, and a match found only in the always-watching tier never counts as something learned.

## Slide 5
MEASURED · 11 PHOTOGRAPHS, FOUR OBJECTS
Every tier got every retrieval right.
Tier | Recall@1 | Margin over best wrong match | Calibrated threshold
long 768d | 100% | +0.043 | 0.331
medium 256d | 100% | +0.038 | 0.361
short 64d | 100% | +0.013 | 0.416
What the tiers actually showed
Colour survives truncation, so two same-shape mugs separated cleanly even at 64 dimensions. What shrinks is margin — the gap to the nearest wrong answer collapses from +0.043 to +0.013. Three times less headroom for the same accuracy. That is the real cost of truncation here, and it is why each tier needs its own threshold.
Notes: Do not claim the 64-dim tier fails. On this set it did not. The margin narrowing is the honest finding.

## Slide 6
MEASURED · THIS RUN
Remembering versus asking.
MEMORY LOOKUP
0.058 ms
Brute-force cosine over the learned tiers. No network, no GPU.
ESCALATION
1–6 s
Round trip to an 11B vision model on an NVIDIA NIM.
PER FRAME STORED
256 B
At 64 dimensions, against 8192 bytes for a fixed-width 2048-dim baseline.
~4,200× fewer operations to answer from memory than to wake the expensive model — and 32× less storage per frame.

## Slide 7
PROJECTED · WAREHOUSE FLEET
92 gigabytes, not three terabytes.
One frame per second of continuous perception, eight-hour shifts, 250 shifts a year. Projected from directly measured bytes per frame.
One robot, one 8-hour shift
32x less
236 MB
7 MB
One robot, one year
32x less
59 GB
1.8 GB
50-robot fleet, one year
32x less
2949 GB
92 GB
fixed-width 2048d
tiered 64/256/768
Notes: Storage is the cleanest projection in the deck — it is arithmetic from measured bytes per frame, derivable on a napkin.

## Slide 8
PROJECTED · COMPUTE AND ENERGY
Five times less perception compute.
If the gate answers eight queries in ten — realistic for a robot working a familiar space — then across 100 queries:
ALWAYS ESCALATE
3,740 TFLOP
Every query wakes the 11B model.
GATED AT 80%
749 TFLOP
80 answered from memory, 20 escalated.
REDUCTION
5.0×
Less perception compute — and, on fixed silicon, roughly 5× less perception energy.
Energy is inferred, not measured. No wattage was recorded on this laptop, and none on a Jetson. Energy is assumed to track compute on fixed silicon. The claim that needs no assumption: every question memory answers is a model invocation that never happens at all.

## Slide 9
SCOPE
What this does not claim.
That the cheap path is faster per call.
Measured false here — local encode ~1.6 s against a hosted VLM at ~1.0 s. The expensive path runs on datacentre GPUs while the encoder runs on laptop CPU. The claim is calls avoided, not latency won.
That truncation saves encoder compute.
It does not. The backbone runs once regardless of dimensions kept.
That anything ran on a Jetson, TensorRT, or Isaac GR00T.
None did. The hosted VLM is a stand-in for the escalation target.
A measured power figure.
None was taken. Energy is inferred from compute and labelled as such.
Stating which figures are measured, which projected and which inferred is the point — not a disclaimer.

## Slide 10
THE STACK
Running today, and what's next.
RUNNING AND MEASURED
jina-clip-v2
local · CPU · open weights, CC BY-NC
llama-nemotron-embed-vl-1b-v2
NVIDIA NIM · fixed-width baseline, 2048d
llama-3.2-11b-vision-instruct
NVIDIA NIM · escalation target
parakeet-ctc-0.6b · magpie-tts
NVIDIA Riva · speech in and out
NEXT STEP · NOT YET RUN
Jetson Orin Nano Super
encoder and memory move on-device
TensorRT
collapses the encoder latency that dominates today
Isaac GR00T N1
replaces the VLM stand-in with a real VLA
The gate does not know what sits behind it — swapping the escalation target is one function call.
44 unit tests · every measurement reproducible · github.com/ankursharma435/robot-semantic-memory